## Slide 1: Packet Chaining: Efficient Single-Cycle Allocation for On-Chip Networks
George Michelogiannakis, Nan Jiang,
Daniel Becker, William J. Dally
Stanford University
MICRO 44, 3-7 December 2011, Porto Allegre, Brazil

## Slide 2: Introduction
Performance sensitive to allocator performance
Packet chaining improves quality of separable allocators
Packet chaining outperforms more complex allocators
  Without the delay of those allocators

## Slide 3: Outline
Motivation
  Separable allocation without packet chaining
Packet chaining operation and basics
Packet chaining cost
Performance evaluation
Conclusions

## Slide 4: Conventional separable allocation
Step 2:
Both output arbiters pick the same input (1)
Step 3:
Input 1 can only pick one output
1
Inputs
2
3
1
Outputs
2
3
Arbitrating independently at each port degrades matching efficiency
  If output 2 was aware of output 1’s decision, it would had picked input 3
Example: output-first separable allocator
Step 1:
Requests propagate to output arbiters
3,2
2,1
1,2
1,1

## Slide 5: Other ways to improve allocation
Increasing the number of iterations
Incremental allocation
  Ineffective for single-flit packets
More complex allocators
  Wavefont:
    3x power and 20% more delay compared to a separable allocator
  Augmenting paths:
    Infeasible in a single cycle (approximately 10ns delay)

## Slide 6: Outline
Motivation
Packet chaining operation and basics
  Maintaining connections across packets
Packet chaining cost
Performance evaluation
Conclusions

## Slide 7: Packet chaining operation
Starting from previous
Example:
Input 1 granted output 1.
This forms a connection
1
Inputs
2
3
1
Outputs
2
3
Key: packet chaining enables connection reuse between different packets destined to the same output as departing packets
  The packets do not have to be in the same input
Example: output-first separable allocator
Next clock cycle:
Input 1 sends another packet to output 1.
Output 2 grants input 3
1,1
1,2

## Slide 8: Packet chaining pipeline
Chaining is performed in the PC stage, before SA
  Newly-arrived flits skip PC if SA does not have another flit. Thus, zero-load latency does not increase
  Connections released if they cannot be used productively
Packet 2 Body
Packet 1 Tail
Cycle 2: At the end of cycle 2, the chaining logic selects packet 2.
Packet 2 will reuse packet 1’s connection
Cycle 3: Packet 2 does not participate in SA. Its inputs
and outputs remain connected, blocking other requests
Packet 2 Head
PC
SA
ST
PC: packet chaining
SA: switch allocation
ST: switch traversal
Packet 1 Head
Packet 1 Body
Cycle 2:
When the tail flit enters the SA stage, the chaining logic considers eligible chaining requests
Cycle
1
Packet 1 Body
Packet 1 Tail
2
Packet 2 Head
Packet 1 Tail
3

## Slide 9: Starvation control
Packet chaining uses starvation control
In practice, connections are released by empty input VCs or output VCs without credits before starvation

## Slide 10: Outline
Motivation
Packet chaining operation and basics
Packet chaining cost
  The impact of adding a second allocator
Performance evaluation
Conclusions

## Slide 11: Packet chaining cost
Eligibility checking is very similar for both allocators
The two allocators are identical and in parallel
Conflict detection required by the PC allocator is simpler than VC selection for the combined allocator
Wavefront requires up to 1.5x more power and 20% more delay in a mesh
PC and SA are in separate logical pipeline stages because they operate on different packets

## Slide 12: Outline
Motivation
Packet chaining operation and basics
Packet chaining cost
Performance evaluation
  Throughput, latency and execution time
Conclusions

## Slide 13: Methodology
8x8 2D mesh with DOR
Baseline iSLIP-1 with incremental allocation
Synthetic benchmarks to stress network
Execution-driven CMP applications
  64 scalar out-of-order CPUs
  CPUs clocked four times faster than network
  Single-flit control packets
  Five-flit data packets (32-byte cache lines)

## Slide 14: Throughput under heavy load
15%
2.5%
6%

## Slide 15: Comparison of saturation points
Chart: Mesh. 1 flit per packet. Saturation throughput
| Uniform | Average
iSLIP-1 | 42 | 26.8
Chaining | 44 | 28.3
Wavefront | 43.5 | 27.7
Augmenting path | 45.5 | 28.5
Increases saturation throughput by 5-6%
  Is comparable to augmenting paths

## Slide 16: Latency
Packet chaining reduces average latency by 22.5%

## Slide 17: The effect of packet length
Throughput gains drop with the increase of flits per packet
  Because incremental allocation becomes effective
However, packet chaining still offers comparable or slightly higher throughput compared to wavefront and augmenting paths

## Slide 18: Application execution results
53% of the packets in our simulations were single-flit
Packet chaining: comparable throughput to wavefront on average
Chart: Throughput increase (%)
| Blackscholes | Canneal | Dedup | FFT | Fluidanimate | Swaptions | Average
IPC increase | 46 | 1 | 6 | 9 | 3 | 29 | 16
Packet chaining versus iSLIP-1 using benchmarks

## Slide 19: Conclusions
Packet chaining outperforms other allocators – even ones that are slower or infeasible in one clock cycle
  True for packets of any length
  Throughput gains increase with single-flit packets

## Slide 20: Questions?
That’s all folks